## Slide 1: From Path to Trajectory: Trajectory Planning for Galvanometer Scanners.
Natakala Dakshesh
TUM PREP

## Slide 2: Agenda
Next Steps
6
Reinforcement Learning
5
Collocation Method
4
Hamilton-Jacobi-Bellman Method
3
Requirements and Existing Model
2
Background
1
Notes: First we’ll go through the background, then we’ll look at methods I tried – only reinforcement learningworked.

## Slide 3: Trajectory Planning: Background
  Paths are unordered lists of positions
  Trajectories are a list of positions, ordered in time
  Trajectories follow paths
  Goal is convert paths to optimal trajectories
  Improve productivity of laser processes
What is it?
Figure 1: Galvanometer scanner. 2 mirrors are attached to motors. Can deflect laser beams onto an x-y plane – used in industrial processes e.g. cutting, welding.
Notes: What is trajectory planning, and why do we need it?
My supervisor has been looking at galvanometer scanners – 2 mirrors attached to motors, deflect laser beams in 2D space
Used for variety of laser based manufacturing processes
To function, they need a trajectory input, which should cover a path.
A path is not a trajectory!!!
Path = underordered list of position e.g. square – doesn’t tell you how the laser beam should cover the square.
Trajectory = list of positions with times.
Goal = convert paths to optimal trajectories.
Improve productivity.

## Slide 4: Trajectory Planning: Background
  Current Methods
  Normally, trajectories are calculated manually, without guarantees that they are optimal
  These are ‘open-loop’ trajectories – they cannot react to live information and fix errors
  They are fed through a PID controller, which makes them ‘closed-loop’, correcting errors
  Why now?
  Laser sources have been increasing in power and falling in price
  More powerful lasers can speed up production processes
  Limitation is no longer laser power to shape material, but finding best trajectory for laser
  Project goal is least time optimality
Figure 2: Comparing path to real trajectories. Black is ideal path. Green and blue are trajectories. Is it faster to accelerate around the corner, or to turn off the laser, do a loop, and continue?
Notes: Next slide: Background II
Why do we need to develop something new? First let’s look at current technology.
Normally, trajectories are calculated manually – not optimal e.g. hard to tell if you have the fastest trajectories.
Open loop trajectories – cannot react to live info/fix random errors.
Fed through PID controller, corrects errors, closed loop – even if the initial trajectory was optimal, probably not after this.
Previously this wasn’t a big problem. However, lasers up power, down price.
Before, calculating the fastest trajectory wasn’t very useful, as laser was bottleneck. Now trajecgtory is – the goal for this project is to find and algorithm to make the fastest trajectories.
See an example in figure 2. Black line is path, green line is one trajectory, blue line is another trajectory.

## Slide 5: Requirements
  Trajectory needs to satisfy pre-existing dynamics model
  Need flexibility to add constraints
  Current high-end lasers require input every 10us
  Need fast computation to update best trajectory depending on errors
  Goal is find the trajectory to follow the path in the fastest time
  Need to be able to specify allowed errors
Existing Dynamics Model
Fast Computation
Least Time Optimisation
1
2
3
  Lorem ipsum dolor sit amet, consetetur elitr
  At vero eos et accusam et justo duo dolores et ea rebum
  Lorem ipsum dolor sit amet, consetetur elitr
  At vero eos et accusam et justo duo dolores et ea rebum
  Lorem ipsum dolor sit amet, consetetur elitr
  At vero eos et accusam et justo duo dolores et ea rebum
Header A
Header C
Header B
Please choose high contrast between Primary and Contrast color
1
2
3
  Methods only need to generate open loop optimal trajectories, which could then have randomised initial conditions to generate training data for a neural network.
  Closed loop solution can then be created.
Neural Networks – Fast method to approximate complex functions
Notes: Requirements:
What does our algorithm need to do?
Firstly, has to use the dynamics model, which predicts the relationship between inputs trajectories and output trajectories.
Secondly, needs to find the fastest trajectory, with error constraints of path. Larger errors = rounder corners, much faster.
Need very fast computation – required for closed loop trajectories reacting to live data, to find new optimal trajectories.
Therefore decided we needed a neural network approach – approximate complex functions quickly, very flexible.
Still need to calculate optimal trajectories to feed into neural network as training data. Create open loop optimal trajectories, a lot easier than closed loop.

## Slide 6: The Dynamics Model
  Existing model is in the Laplace domain – useful for traditional PID controllers.
  T = Tracking Error
  = Empirical Parameter
  Requires complex inverse Laplace transform into time domain.
  Convolution is simpler than inverse Laplace transform
  Acceleration can only be calculated in the time domain
  Inverse laplace transforms of G(s), only valid for integer values of T and t > 0.
  A = normalisation coefficient.
Multiplication -> Convolution
Laplace Domain
Time Domain
  No Acceleration
  Acceleration
  No Acceleration
  Acceleration
Notes: Dynamics Model:
What is the dynamics model I talked about?
The existing model is a transfer function in the frequency domain, as is traditional for PID controllers. To get the output in the frequency domain, multiply the input by the transfer function. Then, inverse laplace transform into time domain.
However, this has multiple problems. Firstly, inverse laplace transforms are computationally expensive, and can be hard to ensure are stable.
Secondly, cannot distinguish between acceleration constant velocity in frequency domain
Therefore, use we can use the convolution theorem to convert the multiplication in frequency into a convolution in time, and only inverse laplace transform the transfer functions. This is much simpler computationally.

## Slide 7: Agenda
Next Steps
6
Reinforcement Learning
5
Collocation Method
4
Hamilton-Jacobi-Bellman Method
3
Requirements and Existing Model
2
Background
1
Notes: Next lets look at the methods I tried.

## Slide 8: Hamilton-Jacobi-Bellman-Equation [1]
2 Fundamental Issues:
  The equation of motion depends on an integral over the trajectory, due to the convolution
  HJB solution returns function u = g(x, t) – for any position/time. However, the next steps must depend on previous steps, so this function does not have enough information.
  Pontagyrin maximum principle is a related method which only finds open loop solutions -> returns function u = g(t) – theoretically allowed
  Problem is least time minimisation – key parameter is integral limits which are fixed.
  Change of variables to position impossible due to integral equation of motion [2].
Convolution
Least Time
Where is an error function which follows the path.
Subject to eq. of motion: and velocity constraints
By solving a PDE, can find the closed loop (error correcting) optimal inputs to minimise the cost function.
Notes: HJB:
First method I tried was HJB. This is a PDE, which solves optimisation problems in a closed loop form.
You define a cost function, which you want to minimise, in the form of an integral. We need 1 + f, as the integral of 1 gives the final time, which we want to minimise, and f is a gaussian function around the path.
You also define the equation of motion, which we have.
However, this method didn’t work: Firstly, the equation of motion is an integral over the previous trajectory. Solving the PDE tells us the optimal input function in terms of space and time, which cannot take into account the previous trajectory – so this won’t work
The other problem is the least time method. A related method can only find open loop solutions, which we can use for training data. However, minimising least time means we change the limits – which is out of the scope of this method.
Researchers have gotten around this by changing variables to position, but we can’t due to the integral equation of motion.

## Slide 9: Collocation: Method [3]
Fundamental Issue:
9
  Cannot set initial conditions – fixed by legendre polynomials
  Causes problems in following the path
Initial conditions
Where is a penalty function to limit velocity.
Subject to eq. of motion:
Same problem setup to HJB method
  Estimate x, u (outputs + inputs) using sum of Legendre Polynomials with different weights
  Discretize in time -> allows approximation of integrals as sums
  Minimise C with respect to weights of polynomials, and the final time – theoretically can quickly find optimum trajectory
Notes: Collocation:
The problem setup is very similar to before, and this method will find open loop solutions, which can make training data.
Firstly we estimate x and u using a weighted sum of polynomials.
Then, we discretize into timesteps. This is important, because it means we can approximate the integrals as sums.
Then we minimise C with respect to the weights, and the final time letting us find the optimum trajectory.
However, we cannot set the initial or final conditions, which causes big problems in following the path.

## Slide 10: Collocation: Results
  Tested 1D path between x = 0 and x = 0.5
  Lack of initial conditions creates unusable results
  Due to waves, final time is not close enough to optimal final time (of 5).
Figure 1: Collocation results for optimal inputs.
Notes: Results:
Here, I tested a 1D path between x = 0 and x = 0.5. The initial value depends on the sum of polynomials, so cannot be set, and makes the result wavy, and unusable. It also doesn’t respect max velocity.

## Slide 11: Agenda
Next Steps
6
Reinforcement Learning
5
Collocation Method
4
Hamilton-Jacobi-Bellman Method
3
Requirements and Existing Model
2
Background
1
Notes: Finally I’ll talk about reinforcement learning, which had some success.

## Slide 12: Reinforcement Learning (RL)
  State and action space are both 2D plane between -1 and +1
  Continuous space – saves on memory instead of finely discretizing
  Implement dynamics model to convert inputs to outputs.
  Implement velocity limiter
  Decided to use A2C – advanced actor critic
  Limited parameters to tune
  Use RNN (recurrent neural networks) which have memory – previous timestep knowledge required to learn integral dynamics model.
  ‘Batch-size’ – number of previous timesteps to feed into RNN
  After each cycle, agent will analyse rewards and learn how to improve
  Key is consistent rewards for each step
  Rewards must be same scale per step
  Two problems: following the path and finding the fastest time.
Environment
Algorithm
Reward
Highly flexible: create an environment and define a reward for positive actions. The algorithm explores the environment and learns the best reward.
Notes: Reinforcement Learning:
Reinforcement Learning is very flexible – you define a reward in an environment, which the algorithm randomly explores, and over time learns the best actions.
The environment can be anything. In our case, it is a 2D plane in continuous space, with our dynamics model to convert inputs to outputs.
Next is the algorithm which trains the agent – this is worth exploring more to see which is the best, but I ended up using A2C.
Inside the algorithm, you need to define neural networks, which learn the actions to maximise reward. I used a recurrent neural network, or RNN – this has memory of previous inputs, which is needed to learn an integral, and is defined by batch size.
The most difficult part to get right is the reward. After each cycle, the agent looks at the rewards for each action, and learns how to improve.
This doesn’t work unless the reward is well defined, has consistent rewards every step and are the same scale. And even then it can fail due to random chance – in theory, multiplying rewards by a constant, or shifting them shouldn’t do anything, but it practice it does.

## Slide 13: Reward Function – Distance based
  Initially tested reward function based on distance from target – failed, probably due to different scales
  Found success with change in distance from target
  Gave end state reward
  Started at (0, 0), goal was (0.5, 0) – max velocity = 0.1
  Can find target, but not optimal time (7 instead of 5.1)
Figure 2: Distance based reinforcement learning, inputs.
Notes: Reward functions:
First I tested just making the agent reach the goal, and the reward was negative distance from the target. This completely failed, probably because of different scale of the rewards.
Instead, change in distance from the target worked, combined with an end state reward.
This didn’t really optimise for least time though. And it also can’t work with arbitrary paths.

## Slide 14: Reward Function – Path Following
  Need to adapt this to follow general path.
  Create standardised reward function
  Flexible – works with any path shape y = f(x)
  , where is distance in the y direction to the path
  At start and end points, use total distance instead
  Slope the function in the direction of travel
  The reward is the change in value – incentivised to travel to the goal along the path.
Figure 3: Value function for path from x = 0 to x = 0.5.
Change in ‘value’ generates reward.
Notes: Therefore I made a more flexible reward function. You input a function form y = f(x). The value is found by looking at the inverse of y away from the path.
At start and end points, use total distance instead.
Finally, slope the function in the direction of travel.
As before, reward is change in this value.

## Slide 15: Results: Straight Line Tests
  Find time is minimised best by adding if successful.
  Tested on 2D plane – goal is path from x = 0 to x = 0.5, max velocity = 0.1
  Succeeds ~82% of the time
  Fastest possible time is 5.1 - successful results are between 5.1 and 5.3
  Parameters are optimised using Optuna, hyperparameter tuner, including tilt of reward function, height of rewards, and RNN parameters.
Figure 4: Value based reinforcement learning, outputs.
Notes: Straight line tests:
To optimise for time, I added 1/(1 + final_time) to the reward end state reward, which was effective. Testing on a path between 0 and 0.5, with speed limited at 0.1, it succeeded 82% of the time.
The fastest possible time was 5.1, and all successful results were very close, at 5.3 or below, showing this has success.
To make this work, I optimised parameters using Optuna, which will probably be needed for each path.

## Slide 16: Future Steps
  Test with more complex paths involving acceleration
  Will likely need pretraining to work – the acceleration transfer function sets constant velocity segments to 0, making it difficult to use.
  Look into allowing the laser to turn off (could be faster at corners).
  Can investigate ‘dynamics randomisation’, letting the agent learn how to deal with random errors
  Unlikely to ever have a high enough success rate to control directly - ~70% is good in RL [4]
  Instead take best results as training data for supervised learning
  Continue to tune hyperparameters + reward function.
  Make Optuna multithreaded to take full advantage of HPC.
  Test different reinforcement learning algorithms e.g. PPO, SAC
More Paths
Closed Loop
Tuning
Notes: Future Steps:
3 things are required to research. The first is more paths – we need more than a straight line. The more complex the path, especially if it accelerates, the harder it is to reach the goal – we probably need pretraining.
We could also give the environment more flexibility e.g. turning the laser on/off.
Secondly, we need to make it closed loop – dynamics randomisation is a method to do it in reinforcement learning, but the success rate will probably never be high enough to trust – 70% is seen as a good result in reinforcement learning.
Instead, use to generate slightly randomised training data for supervised learning.
Finally, we can tune more to improve performance, by making optuna multithreaded, or using more complicated RL algorithms.
Thanks for listening.

## Slide 17
Natakala Dakshesh
  TUM PREP
[1] M. Bardi and I. C. Dolcetta, Optimal Control and Viscosity Solutions of Hamilton-Jacobi-Bellman Equations. Boston, MA: Birkhäuser, 1997.
[2] D. Verscheure, B. Demeulenaere, J. Swevers, J. De Schutter, and M. Diehl, “Time-optimal path tracking for robots: A convex optimization approach,” IEEE Transactions on Automatic Control, vol. 54, no. 10, pp. 2318–2327, 2009. doi:10.1109/tac.2009.2028959
[3] N. Negarchi and K. Nouri, “A new direct method for solving optimal control problem of nonlinear Volterra–fredholm integral equation via the Müntz–Legendre polynomials,” Bulletin of the Iranian Mathematical Society, vol. 45, no. 3, pp. 917–934, 2018. doi:10.1007/s41980-018-0173-z
[3] A. Pan, “Deep Reinforcement Learning doesn’t work yet,” Sorta Insightful, https://www.alexirpan.com/2018/02/14/rl-hard.html (accessed Aug. 25, 2023).
References

## Slide 18: Methods
  Text
  Text
  Text
  Text
Text
Text
Text
Text
  Approximate input and output using polynomial basis set
  Discretise trajectory into timesteps
  Define cost function in terms of input and output, and estimate by summing over timesteps
  Minimise cost function by altering polynomial parameters, generating trajectory.
  Randomly generate training data by altering initial conditions
  Define cost function C(x, u, t) as integral over path, which will be minimised
  Cost function is subject to constraint , where u is the input
  Solve PDE to find minimum value of C(x, u, t)
  To calculate u, the optimal input, minimise C(x, u, t) with respect to u.
  Can provide analytic solution, which can be approximated by a neural network
  Create custom environment, with allowed ‘states’ and ‘actions’
  Agent, modelled by a neural net, initially randomly selects actions
  Over time, will analyse rewards for each action, and improve selection to reach goal
  Agent can either directly control, or be used to generate training data
  Long training times and difficult to tune, but highly flexible
Collocation
Hamilton-Jacobi-Bellman Equation
Reinforcement Learning

## Slide 19: Appendix: Parameters for successful tests
tilt_factor = 0.7, prob_factor = 2.8, lr = 0.00383, entropy_coeff = 0.4, hidden_dim = 128, num_layers = 5, gamma = 0.9, batch_size = 50, episode_no = 500, end_reward = 1.5, cuttoff_time = 15,
Batch size is 5s (I used timestep of 0.1, so 50), as this was the length of the transfer function I used in the time domain.

## Slide 20: Appendix: The HJB
Note k is the eq. of motion. Solve the PDE for V, then minimise for u, the input.

## Slide 21: Backup: New Agenda